## Slide 1
OXYGEN TENSION AND BLOOD VELOCITY MEASUREMENTS IN SINGLE CORTICAL MICROVESSELS DURING NORMOVOLEMIC HEMODILUTION
Eugene P. VOVENKO1), Aleksander S. GOLUB2) and Roland N. PITTMAN2)
1) -  Pavlov Institute of Physiology, nab. Makarova, bld.6, St.-Petersburg, 199034, Russia, tel: +7 (812) 3280701 Ext.141, fax: +7 (812) 3280501, e-mail: epv@infran.ru
2) -  Department of Physiology, Medical College of Virginia Campus, Virginia Commonwealth University, Richmond, VA 23298, P.O. Box 980551, tel.: +101 (804) 8289545,
fax: +101 (804) 8287382, e-mail: pittman@hsc.vcu.edu
ABSTRACT
We measured Po2 and blood velocity on the same (single) venules (18.6±2 µm, mean±SE) of rat brain cortex during normovolemic hemodilution (exchange transfusion with 6% hetastarch, "HESPAN"). The phosphorescence quenching technique was applied for intravascular Po2 measurements. Blood velocity in venules was assessed using 2 µm diameter fluorescent microspheres, 100 Hz flash illumination and frame-by-frame analysis of video recordings.
At control (Hct=44%, MAP=130±4 mm Hg) venular Po2 was 38.5±3.0 mm Hg and blood velocity was 1109±108 µm/s. The first step of hemodilution (Hct=34%, MAP=131±3 mm Hg) resulted in a significant increase of microvascular Po2 (43.3±3.0 mm Hg) and blood velocity (1560±150 µm/s). The second step of hemodilution (Hct=20%, MAP=121±3 mm Hg) was accompanied by a moderate fall of microvascular Po2 (34.1±2.2 mm Hg) relative to the control level and an increase in venular blood velocity (2271±220 µm/s). The third step of hemodilution (Hct=11%, MAP=109±3 mmHg) induced a sharp decrease in venular Po2 (21±3 mm Hg), while blood velocity in venules increased steadily to 2433±144 µm/s.
In conclusion, the first step (mild) of hemodilution resulted in a significant increase of oxygen delivery to brain tissue, while the second (moderate) and especially third steps (severe) indicated increased stress on the oxygen transport system and signs of developing hypoxia.
Hemodilution is widely used in clinical medicine (vascular, cardiac surgery, orthopedics, etc.). Replacing whole blood with a crystalloid fluid reduces blood viscosity, improves cerebral blood flow and enhances oxygen delivery to tissue, minimizing disturbances at the microcirculatory level [1,4]. Few studies, however, focus on the effect of anemia on brain oxygenation at the level of tiny microvessels, where the bulk of oxygen exchange between blood and tissue take place.
The aim of the present work was to develop a new experimental approach for measuring microvascular oxygen tension on small brain cortical arterioles and venules using the phosphorescence quenching technique.
Using this approach two main parameters of oxygen transport to tissue (microvascular pO2 and blood velocity) in the same microvessels of brain tissue during control conditions and during isovolemic hemodilution were measured for the first time.
RESULTS
SPECIFIC AIMS
METHODS
Isovolemic hemodilution to Hct=34% (mild) resulted in a significant increase of blood velocity (and blood flow) in small cortical venules draining blood directly from capillaries. Augmentation of the pO2’s in the same microvessels indicated an enhancement of the oxygen supply to brain tissue.
Hemodilution to Hct=20% (moderate) indicated increased stress on the oxygen transport system to brain tissue. Microvascular pO2 was close to the control values, while blood velocity in venules was significantly elevated.
The third step of hemodilution (severe) to Hct=10% resulted in a further increase of venular blood velocity, while oxygen tension in the same venules fell significantly, indicating signs of developing hypoxia.
A new technical approach was developed to provide immediate measurements of pO2 on small cortical microvessels using the phosphorescence quenching technique, and measurements of blood velocity in the same venules using the fluorescent FluoSphere tracking technique.
CONCLUSIONS
Ten male Sprague-Dawley rats, 280±4 g bw were anesthetized by ip injection of Na-pentobarbital, surgery dose – 65 mg/kg, supplemental dose - 10-15 mg/kg/h. Animals were tracheotomized with plastic tubing (PE-240) to ensure proper lung ventilation; PE-90 catheters were inserted into right femoral artery and vein for MAP monitoring, blood gas analysis sampling, blood exchange transfusion and for infusions.
A Closed Cranial Window (CCW) was made over the right parietal lobe (hemisphere). Perfusion of the window was performed using a peristaltic mini-pump (Daigger and Company, Inc., Lincolnshire, IL) with a rate of 0.3-0.5 ml/min. Intracranial pressure (ICP) was kept about 4-6 mm Hg by the elevation of the outflow reservoir.
An intravital microscope (Carl Zeiss, Hawthorne, NY) equipped with a Neofluar 25X/0.60 N.A. objective was used to visualize brain cortex microvessels. Epi-illumination of the brain surface was performed using a Fiber-Lite MI-150F illuminator (Dolan-Jenner Industries Inc., Lawrence, MA). The optical fibers were positioned at a 50° angle (relative to the optical axis) and two light spots were focused on the focus plane of the objective.
Microvascular oxygen tension was measured using the phosphorescence quenching technique. A phosphor solution was injected intravenously at the beginning of the experiment to yield an estimated plasma concentration of 0.3-0.5 mg/ml. A xenon flash lamp (model FX-249, EG&G Electro-optics Co., Salem, MA; 10 Hz flash frequency, power 2.5 J) was used for phosphor excitation. The size of the excitation window was set by a rectangular diaphragm. The smaller dimension of the rectangular window was equal in length to the inside diameter of the vessel being measured. The emitted phosphorescence passed through a dichroic mirror and through a 630 nm cut-on filter and was detected by a photomultiplier tube (model R632, Hamamatsu Photonics, Japan). The amplified output was sent to a data acquisition board in a personal computer. Fifty decay curves (elapsed time 5 s) were collected for each measurement site in order to improve the signal-to-noise ratio through signal averaging. Data acquisition was under the control of a LabView program (version 4.1, National Instruments, Austin, TX).
Blood velocity measurements in venous cortical microvessels were performed using fluorescent microspheres (FS), injected into the blood stream, flash illumination and frame-by-frame analysis of the tracks on video recordings [2]. Fluorescent microspheres, 2 µm in diameter, type F-8827, yellow-green 505/515 nm (Molecular Probes , Inc., Eugene, OR) were injected intravenously, as a 0.1-0.2 ml bolus in a concentration of 1·108 ml-1. This quantity of particles was enough to provide measurements of linear blood velocity in venules of luminal diameter of 10-100 µm over a 2-3 minutes period.
For technical reasons velocity in arterioles using FS-method was not measurable.
Ten male Sprague-Dawley rats were used in the study.
Hemodilution to Hct=34% (first step) induced no significant changes in systemic variables from control.
The second step of hemodilution (Hct=20%) resulted in a decrease of MAP to 120.5±2.8 mm Hg (p<0.05).
Severe hemodilution (Hct=10%) produced a sharp decrease in MAP to 108.8±2.5 mm Hg (p<0.001), arterial pCO2 to 32.3±1.1 mm Hg (p<0.001) and arterial pO2 to 73.6±1.4 mm Hg (p<0.0001).
REFERENCES
Duebener L. F., et al. (2001) Effects of hematocrit on cerebral microcirculation and tissue oxygenation during deep hypothermic bypass. Circulation 104 (12 Suppl 1):I260-I264.
Rovainen C. M., Wang D. B., and Woolsey T. A. (1992) Strobe epi-illumination of fluorescent beads indicates similar velocities and wall shear rates in brain arterioles of newborn and adult mice. Microvasc.Res. 43 (2):235-239.
Vovenko E.P. Distribution of oxygen tension on the surface of arterioles, capillaries and venules of brain cortex and in tissue in normoxia: an experimental study on rats. Pflügers Arch. 437(4):617-623, 1999.
Tomiyama, Y. et al., (1999) Hemodilution, cerebral O2 delivery, and cerebral blood flow: a study using hyperbaric oxygenation. Am.J.Physiol. 276:H1190-H1196.
The objective of the microscope was always focused on the median plane of a venule to record FS’s moving only in the centerline. The depth of field of the objective (distance in the vertical plane where all objects are clearly visible), however, is about 3-5 µm. This means that in addition to axially positioned FluoSpheres with maximal velocity, FluoSpheres from different points of a vessel's lumen were also taken into account. The actual blood velocity in the observed venules might thus be higher than the values presented in the Fig.4.
It should be noted that oxygen tension in arterioles was significantly lower than corresponding values of systemic pO2. This pO2-drop was accounted for by O2-diffusion through the arteriolar wall [3].
Mild hemodilution (Hct=34%) resulted in increase (NS) of venular pO2.
Moderate level of hemodilution (Hct=20%) resulted in marked decrease (NS) in arteriolar pO2 and produced no changes in venular pO2 relative to the control. These data indicate the adequate level of oxygen supply to brain tissue, despite the increased stress of oxygen transport mechanisms.
Severe hemodilution (Hct=11%) invoked a pronounced and significant drop (p<0.01) both arteriolar and venular values of oxygen tension. The level of oxygen supply to brain cortex is insufficient with signs of developing hypoxia.
FIGURE 1