## Slide 1
VOVENKO E.), GOLUB A.), PITTMAN R.)
MICROVASCULAR PO2 AND BLOOD VELOCITY MEASUREMENTS IN RAT BRAIN CORTEX DURING NORMOVOLEMIC HEMODILUTION
WITH A PLASMA EXPANDER (HESPAN) AND A HEMOGLOBIN-BASED OXYGEN CARRIER (DCLHb).
) - Pavlov Institute of Physiology, St. Petersburg, RUSSIA;
) - Department of Physiology, Medical College of Virginia Campus, Virginia Commonwealth University, Richmond, the U.S.A.

## Slide 2
OXYGEN SUPPLY TO BRAIN TISSUE
  Microcirculation of brain cortex in rats.
  Measurements in single microvessels.
  Oxygen tension (PO2) in arterioles and venules.
  Velocity in venules.

## Slide 3
OXYGEN SUPPLY IN BRAIN TISSUE:
NORMOVOLEMIC HEMODILUTION
Normovolemic hemodilution
Decreased systemic hematocrit (Hct)
Hemodilution   Hct
Viscosity   Flow
O2 carrying capacity
O2 delivery = Flow x [O2]

## Slide 4
ANIMAL PREPARATION
  Male, Sprague-Dawley rats
  Body weight = 280 15 (SE) g, n = 16
  Closed cranial window

## Slide 5
CLOSED CRANIAL WINDOW
  Over right parietal cortex
  Mock CSF-superfused cortical surface (0.3 – 0.4 ml/min)
  Intracranial pressure (4 – 6 mm Hg)

## Slide 6
OXYGEN TENSION MEASUREMENTS
Phosphorescence quenching microscopy
Palladium meso-tetra [4-carboxyphenyl] porphine
Intravascular injection (plasma concentration of 0.3-0.5
mg/ml )
Lifetime of phosphorescence decay
PO2 from Stern-Volmer equation

## Slide 7
VELOCITY MEASUREMENTS
Fluorescent microspheres, 2 µm in diameter, yellow-green
505/515 nm (Molecular Probes , Inc., Eugene, OR);
iv injection of 0.1-0.2 ml bolus in a concentration of 1·108 ml-1
100 Hz flash illumination
Measure distance traveled between flashes

## Slide 8
ISOVOLEMIC HEMODILUTION PROCEDURE
Simultaneous infusion/withdrawal of hemodiluent/blood
Infusion/withdrawal rate = 0.6 ml/min
Hct steps: 42 (control), 34, 20, 10 %

## Slide 9
ISOVOLEMIC HEMODILUTION FLUIDS
HESPAN (6% Hetastarch) – Plasma expander
DCLHb (diaspirin cross-linked hemoglobin; Baxter
Hemoglobin Therapeutics) – Hemoglobin-based oxygen
carrier (HBOC)

## Slide 10
SCHEMATIC DIAGRAM OF SETUP

## Slide 11
RESULTS: Blood Velocities in Pial Venules during Hemodilution with HESPAN and DCLHb

## Slide 12
RESULTS: HESPAN – PO2 vs HCT

## Slide 13
RESULTS: DCLHb – PO2 vs HCT

## Slide 14
SUMMARY OF RESULTS
HEMODILUTION
VELOCITY – progressive increase (Hespan)
– increase to plateau (DCLHb)
PO2 – progressive decrease (Hespan)
– approximately constant (DCLHb)

## Slide 15
CONCLUSION
DCLHb provides effective oxygenation of the brain cortex in the rat, even under conditions of severe hemodilution.

## Slide 16
ACKNOWLEDGEMENTS
This work was supported in part by the National Heart, Lung and Blood Institute, and the A.D. Williams Trust Funds (Virginia Commonwealth University).
ADDRESSES for CORRESPONDENCE:
Eugene VOVENKO – vovenko@infran.ru
Roland PITTMAN – pittman@hsc.vcu.edu